## Slide 1: MEPRFP Automation 2.0
A Revit panel for repeatable MEP layouts
Equipment profiles · Spaces · Circuiting

## Slide 2: Why we built this
MEP layouts are repetitive across stores / project types — the same fixtures land in the same relative spots over and over.
Hand-laying each instance burns hours and produces inconsistent output across projects and engineers.
MEPRFP Automation 2.0 lets us capture a layout once as a reusable template, then place it everywhere it's needed.
Templates live as project-local data plus exportable YAML, so they round-trip across projects cleanly.

## Slide 3: What's in the panel
Import-Export Profiles — YAML in / out for sharing.
Modify Profiles — author and edit equipment templates.
Place from CAD or Linked Model — drop equipment from a host model or DWG block layout.
Place Single Profile — one-off placement at a picked point.
Place Element Annotations — tags, keynotes, text notes.
Spaces — bucket-based templates anchored to room geometry.
Circuiting — SuperCircuit V5 builds Revit electrical systems from the captured fixtures.
Audit tools — find drift between YAML and the live model.

## Slide 4: The profile model
A profile is a YAML record describing a parent fixture and the linked elements (LEDs) that travel with it.
Each LED carries: family : type label, parameters, offsets, and an annotation list (tags / keynotes / text notes).
Offsets are expressed in the parent's local frame — so when a parent rotates, every linked element rotates with it.
Profiles support truth-source merge groups so a fix in one definition propagates to every member of its group.

## Slide 5: Where the data lives
All project-local data sits in Extensible Storage on a dedicated DataStorage element (not on ProjectInformation).
Two ES schemas — equipment YAML and space classifications — are kept on separate DataStorages so an export of one doesn't drag the other.
v4 schema layout: four typed map fields (String / Bool / Int64 / Double) plus a DocGuid string. Int64 with Int32 fallback keeps Revit 2026 happy.
Legacy v1 entities (simple-fields layout on ProjectInformation) still read; first save migrates the data forward without GUID changes.

## Slide 6: Equipment workflow — author
Select a parent fixture in Revit + run Capture.
The capture engine walks every linked element, records family : type, parameters, offsets relative to the parent, and any tags / keynotes / text notes near it.
The captured profile lands in the active project's YAML store — Manage Profiles lets you rename, merge, edit, and delete entries afterward.
Element_Linker JSON is stamped on every captured element so audits can match each placed element back to its profile.

## Slide 7: Equipment workflow — place
Place from CAD or Linked Model: pick a host doc (linked Revit, DWG block layout, or CSV) and the engine matches every parent target to a profile, then drops every LED at its captured offset.
Place Single Profile: pick a point in the host view, choose a profile from the active store, and the engine creates the family instances at the offsets.
Place Element Annotations: walks placed fixtures, looks up their LED's annotations list, and creates tags / keynotes / text notes — already-placed items are deduped by default.

## Slide 8: Circuiting — SuperCircuit V5
Reads the CKT_Panel_CEDT, CKT_Circuit Number_CEDT, CKT_Load Name_CEDT, CKT_Rating_CED, and CKT_Schedule Notes_CEDT parameters off captured fixtures.
Groups fixtures into circuits (DEDICATED, BYPARENT, SECONDBYPARENT, NORMAL) and creates Revit ElectricalSystem objects via an ExternalEvent gateway.
Client-aware: HEB and Planet Fitness keyword sets are handled by per-client classifier modules with a shared base.
Audit Circuits surfaces drift between YAML and live circuits — missing data, phantom panels, orphan circuits, pole mismatches.

## Slide 9: Spaces — bucket vocabulary
Buckets are keyword-tagged categories like RESTROOM, BAKERY, ELECTRICAL ROOM. Each bucket has a list of case-insensitive substring keywords + an optional client-key restriction.
Manage Space Buckets lets the user define / edit the vocabulary directly in Revit.
Classify Spaces walks every placed Revit Space, matches its name against bucket keywords, and lets the user override per-space (multi-bucket assignment supported).
Classifications are project-local — they don't ride with exported templates.

## Slide 10: Spaces — profiles & door-aware anchors
A space profile is a template entry that targets a bucket and lists LEDs to place inside any matching space.
Multiple profiles can target the same bucket — they stack, so a Restroom space gets every Restroom profile's elements.
Anchor kinds (no cardinals — door-aware): center, door_relative, wall_opposite_door, wall_right_of_door, wall_left_of_door, corner_furthest_from_door, corner_closest_to_door.
Manage Space Profiles edits buckets, profiles, LEDs, parameters, offsets, and annotations end-to-end without touching YAML by hand.

## Slide 11: Spaces — placement flow
Place Space Elements collects every classified space, finds matching profiles, and previews every prospective family instance in a flat selectable table.
If a space has more than one door AND a door-dependent anchor, the user is prompted to click the reference door in the model (host or linked) — that choice is reused for every door-anchored LED in that space.
Per-row Select checkbox + Bucket column let the user place subsets (e.g. all bakery profiles, none of the freezer ones) without re-classifying.
Place Space Annotations walks placed space-based fixtures and drops their tags / keynotes — same dedup machinery as the equipment side.

## Slide 12: Sharing across projects
Import / Export YAML File round-trips equipment definitions between projects. Output is byte-identical to the stored payload — Import → Export is lossless.
Import / Export Space Config writes only the space-template data (buckets + profiles), never the per-project classifications. A bakery template moves to the next store without taking that store's space-to-bucket assignments with it.
Blank-file imports synthesise an empty v100 payload, so a fresh project can start empty and be built up using the in-Revit editors.

## Slide 13: Element_Linker — the audit backbone
Every placed element gets a JSON payload written to its Element_Linker shared parameter at placement time.
Equipment fields: led_id, set_id, location, rotation, parent rotation, host name, level, facing, parent location, ckt_panel, ckt_circuit_number.
Spaces fields (Stage 6): space_id, space_profile_id — lets audits prove every space-based element back to the Space and template that produced it.
Audit / sync tools use this lineage to detect drift, phantom elements, and missing-data conditions.

## Slide 14: What's next
Smoke-test the full Stage 6 + Stage 7 flow in a real project (in progress).
Optional bucket auto-rerun on classification changes — today re-classification is manual.
Field-feedback iteration on the door picker UX (status-bar prompts vs. a persistent overlay).
Extend audits to surface profile-vs-element drift on the Spaces side (parity with equipment-side Sync Audit).
Continue documenting per-client keyword sets so new clients onboard via a small adapter rather than core code.